## Slide 1: Introduction to VHDL

## Slide 2: What and Why is HDL?
In software everything is sequential
In hardware events are concurrent
Advantages –
  Documentation 
  Simulation of the behavior of the circuit 
  Synthesis – automatic generation of net lists
  Portability
Examples – ABEL, VHDL, Verilog
Notes: ABEL (Advanced Boolean Equation Language)

## Slide 3: VHDL
VHDL is an industry standard language used to describe hardware from the abstract to concrete level.
V – VHSIC - Very High Speed Integrated Circuit
HDL - Hardware Description Language

## Slide 4: BASIC FEATURES OF VHDL
Concurrency.
Supports sequential statements.
Supports for test & simulation.
Strongly typed language.
Supports hierarchies.
Supports for vendor defined libraries.
Supports multivalued logic.

## Slide 5: CONCURRENT AND SEQUENTIAL STATEMENTS
Concurrent - statements are executed at the same time in parallel, as in Hardware
Sequential - it executes one statement at a time in sequence only

## Slide 6: 4 Classes of VHDL statements
• LIBRARY - a file which includes predefined hardware component declarations,
• PACKAGE - a file which includes shared data type definitions in one file
• ENTITY - specifies a logic block with its exact I/O ports
• ARCHITECTURE – describes the internal architecture of the entity
a. Structural Description - the design is represented as an arrangement of interconnected components.
b. Dataflow Description - represents the behavior but implies some structure. It is similar to an RTL description.
c. Behavior Description - describes the behavior of the circuit without any structural information. The description is done using a sequence of programming language statements.

## Slide 7: IEEE Libraries and Packages
The library “ieee” contains several packages of definitions standardized by IEEE, which can be used in all IEEE-certified VHDL environments
Library Package Contents
ieee std_logic_1164 standard data types (bit, byte..)
ieee std_logic_arith signed and unsigned numbers, converters
ieee std_logic_signed signed numbers only
ieee std_logic_unsigned unsigned numbers only

## Slide 8: Entity Declaration
Specifies the interface with the external environment.
Format
  entity NAME_OF_ENTITY is
  port (signal_names: mode type;
  signal_names: mode type;
  :
  signal_names: mode type);
  end [NAME_OF_ENTITY] ;
Entity may have several ARCHITECTURE statements

## Slide 9: Example

## Slide 10: ARCHITECTURE
An architecture specifies the behavior, function, interconnections and the relationship between the inputs and the outputs of an entity.
An entity can have more than one architecture .
There can be no architecture without an entity .
Each architecture is bound to an entity using the configuration statement .

## Slide 11: VHDL architectures can be classified as
Behavioral – Defines a sequentially described functioning of the design.
Structural – Defines interconnections between previously defined components.
Dataflow – Defines a concurrently described functioning of the design.
Mixed - A combination of structural and behavioral architectures .

## Slide 12: Syntax
architecture architecture_name of entity_name is
[declarations]
begin
[statements]
end [ architecture_name ];

## Slide 13: Process Statement
It is a concurrent statement , which delineates a part of an architecture where sequential statements are executed.
Syntax
label: process[(sensitivity list )]
declarations
begin
sequential statements
end process;

## Slide 14: VHDL IDENTIFIERS
Identifiers are used to name items in a VHDL model.
A basic identifier may contain only capital ‘A’ - ’Z’ , ‘a’ - ’z’, ‘0’ - ’9’, underscore character ‘_’
Must start with a alphabet.
May not end with a underscore character.
Must not include two successive underscore characters.
Reserved word cannot be used as identifiers.
VHDL is not case sensitive.

## Slide 15: OBJECTS
There are three basic object types in VHDL
• Signal : represents interconnections that connect components and ports.
• Variable : used for local storage within a process.
• Constant : a fixed value.
The object type could be a scalar or an array

## Slide 16: Data Types
Predefine
  Package standard of library std: BIT , BOOLEAN, INTEGER, REAL
  Package std_logic_1164 of library ieee: STD_LOGIC, STD_ULOGIC
  Package std_logic_arith of library ieee: SIGNED, UNSIGNED
User defined

## Slide 17: Bit literal
Used to represent value of a digital system
Values allowed are 0 and 1
Bit vector literal is expressed as a string of bit literals enclosed in double quotes
e.g. 1 , 0, 1011 , X 7CEF ( hex ), O 5673 ( octal )
e.g. signal valid : bit

## Slide 18: Std_logic type
std_logic type is a data_type defined in the std_logic_1164 package of IEEE library
It defines a number of states for a digital signal which helps in simulation and debugging
It is an enumerated type and is defined as
type std_logic is (U,X,0,1,Z,W,L,H,-);
where
U -Uninitialized
X -Forcing Unknown
0 -Forcing 0
1 -Forcing 1
Z-High Impedance
W -Weak Unknown
L -Weak 0
H -Weak 1
- -Don't Care

## Slide 19: Boolean literal
represents true or false value
values allowed are
  true(TRUE,True)
  false(FALSE,False)
e.g.: signal busactive : boolean;
...
busactive <= true;
...
if (busactive and valid = “1”) then
data_out <= din;
valid_out <= “1”;
end if;

## Slide 20: Character literals
The package STANDARD predefines a set of character literals
Character literals are enclosed in single quotes
e.g. : “a” , “A”, “1” , “!”
An array of character literals is enclosed in double quotes
e.g. “Warning : timing violation”
Not synthesizable

## Slide 21: Integer literal
defines a value with integers
They can be either positive or negative
exponents have to be integers
e.g. 3, -1, 47E23 , -4E-2, 345
16#3ed2# , 16#23#E+2 (base16)
2#10111# , 2#10101#E12 (base2)
e.g. Signal count integer range 0 to 255;
Synthesizable

## Slide 22: Real literal
defines a value with real numbers
They can be either positive or negative
exponents have to be integers
e.g. 3.23, -1.78946, 4.78E23 , -4.23E-2, 0.345
16#1.23ed2# , 16#23.0#E+2 (base16)
2#1.0111# , 2#1.0101#E-12 (base2)
Not synthesizable

## Slide 23: Synthesizable Data Type

## Slide 24: Physical literal
Physical literal is a number with units.
type current is range -2147484638 to 2147484637
units
nA; --Base Unit nano ampere
uA = 1000 nA; --micro ampere
mA = 1000 uA; --milli ampere
A = 1000 mA; --ampere
end units;
Not synthesizable

## Slide 25: Subtype
Subtype is a type with a range constraint
Subtypes are compatible with their base type
subtype Count16 is integer range 0 to 16;
subtype digit is integer range 0 to 9;
subtype nanosec is time range 0 ns to 1 us;

## Slide 26: OPERATORS
Precedence Operator Class Operators
Logical operator and or nand nor xor xnor
Relational operator = /= < <= > >=
Shift Operator sll srl sla sra rol ror
Adding Operator + - &
Sign + -
Multiplying Operator * / mod rem
Miscellaneous ** abs not

## Slide 27: Composite Data Type –Array
There are two composite types
  arrays : contain many elements of the same type
  records : contain elements of different types
Arrays can be either uni or multi dimensional.
Array Declaration Syntax
type array_name is array (index range) of element_type;
examples:
type byte is array (7 downto 0) of std_logic;

## Slide 28: Array Declaration examples
signal A : std_logic_vector(3 downto 0) := “1011”;
signal B : std_logic_vector(0 to 3) := “1011”;
signal C : std_logic_vector(6 downto 0);
A(3) A(2) A(1) A(0)
1 0 1 1
B(0) B(1) B(2) B(3)

## Slide 29: Array assignment examples
A <= („1‟, „0‟, others => „0‟); --aggregation
A <= “1011”;
A <= “10” & ”11”; --concatenation
A <= ( „1‟, „0‟, „1‟, „1‟);
A <= “101” & „1‟;
A <= „1‟ & ‟0‟ & ‟1‟ & ‟1‟;
C <= A & B;
A <= C( 5 downto 2 ); --slicing
A(2 downto 1) <= C(6 downto 5);
A <= (others => „0‟);
A <= (1 => „0‟, others => „1‟ );
A <= (2 | 0 => „1‟ , others => „0‟);
A <= (0 to 3 => „0‟);

## Slide 30: Multi dimensional Array
type array_name is array (index_range, index_range) of element_type;
e.g.:
type memory is array(3 downto 0, 7 downto 0) of bit;
--4 X 8 memory

## Slide 31: VHDL Object types : Signal 
Syntax
Signal signal_name : signal_type [ range constraint ] [:=initial value]
It connects design entities together and communicate changes in values within a design .
Signals can be declared in an entity (can be seen by all the architectures of the entity) , in an architecture (local to the architecture), in a package (globally available to the user of the package) or as a parameter of a subprogram(i.e.. a function or a procedure)
Signals declared in a port statement of an entity describe the components input/output connectors.
Signals have three properties attached to it
–type and type attributes
–value
–time ( i.e. it has a history )

## Slide 32: Signal contd.
signal assignment is done using the „<=„ symbol . e.g. : c <= “1” ;
signals updates can have a delay specified in their assignment statements. E.g..
clk <= not clk after 10 ns;
signal assignment is concurrent outside a process and sequential within a process

## Slide 33: Signal contd.
Concurrent
a <= b;
a <= c; --multiple drivers
Sequential (inside process)
a <= c;
if ip = “1” then a <= b;
end if;
Sequential (inside process)
count <= count + 1;
count <= count + 1;
count <= count + 1;
--count increments only once

## Slide 34: Variable
Syntax
variable variable_name : variable_type [ range ] [:= initial value ];
e.g. : variableindex : integer range 0 to 15;
variablecount : std_logic_vector( 3 downto0 ) := “0000”;

## Slide 35: Variables contd..
Variables are assigned values using the := symbol
Variables are identifiers within a process or a subprogram. Their visibility is limited only to its process or sub program.
Variables have only type and value attached to it. They don‟t have a past history unlike a signal. Require less memory and result in fast simulation.
Variable assignment occurs immediately.

## Slide 36
Sequential (inside process)
count :=count + 1;
count :=count + 1;
count :=count + 1;
--count increments 3 times

## Slide 37: Constant
A constant is an identifier with a fixed value
Syntax
Constant constant_name : constant_type [:=value ] ;
e.g. : constantpi : real := 3.147592;
constantdatawidth : natural := 32;
It is used in place of the value to make the code more readable
A constant has just the type and value associated with it .
Value can be assigned to a deferred constant later in a package if changes are foreseen. This minimizes recompilation.
Constants are used to define data parameters (buswidth, time delay, etc) and lookup tables (ROM , etc);